## Slide 1: Network Design for an Institute
By: Dr. Seema Anand Ladhe

## Slide 2: Link of Network Design
https://drive.google.com/file/d/1BrbkgN4HLihBcHQ-Z3069TmDWr9_cbLS/view?usp=share_link

## Slide 3: Network Design for an Institute
Let the institute is having 4 departments.
Each department is having 3 labs.
Each lab consist 23 systems/computers and one 24 port switch.
The Institute is having one high configures multilayer switch (L2 core Switch).

## Slide 4: Network Design for an Institute..
Using L2 core switch, 4 VLANs are created, one for each department.
Gateway addresses for VLAN are
  VLAN1: 10.1.1.1/24
  VLAN2: 10.1.2.1/24
  VLAN3: 10.1.3.1/24
  VLAN4: 10.1.4.1/24

## Slide 5: Network Design for an Institute..
For VLAN 1:
  Netid: 10.1.1.0/24
  Broadcast address: 10.1.1.255
For VLAN 2:
  Netid: 10.1.2.0/24
  Broadcast address: 10.1.2.255
For VLAN 3:
  Netid: 10.1.3.0/24
  Broadcast address: 10.1.3.255
For VLAN 4:
  Netid: 10.1.4.0/24
  Broadcast address: 10.1.4.255

## Slide 6: Network Design for an Institute..
The institute is having one router to connect to the outside world (Network).
The traffic between all VLANs and Router passes via trunck port of VLAN and virtual interfaces.
NAT routing for each VLAN is configured on router.
Router is connected to the network of ISP using the public IP given by an ISP.

## Slide 7: Link for Feedback
https://forms.gle/WKREna3zAUfuakJ78

## Slide 8
Thank you